## Slide 1: TeenyAT Robot Architecture
/ˈtē∙nē∙ət/
An Architecture to Virtualize

## Slide 2: Core Architectural Elements
16 bit words (each memory address points to a 16 bit value)
32K words of RAM from 0x0000 through 0x7FFF
Address 0x8000-0xFFFF: available for hardware access
8 registers available to all register-use instructions
  pc (or r0) is the program counter, contains address of next instruction, initially 0x0000
  r1 through r6 are general purpose registers
  sp (or r7) is the stack pointer, contains address below top element, initially 0x8000 (empty)
Instructions encoded in either one or two 16 bit words
  Fetch must set PC = PC + 1 + the "teeny" bit to account for this
    if teeny == 0, it's 16 bits (essentially assumes 2nd word is 0x0000)
    if teeny == 1, it's 32 bits and requires an additional cycle

## Slide 3: Instruction Set
Arithmetic (dreg,sreg)
add
sub
mult
div
mod
neg reg
*inc reg
*dec reg
Logic (dreg,sreg)
and
or
xor
inv reg
shf dreg, imm
rot dreg, imm
bts dreg, imm
btc dreg, imm
btf dreg, imm
Data
set dreg, imm
load dreg, addr
stor addr, sreg
push sreg
pop dreg
Control
call addr
ret*
bra addr*
bl, ble, be, bne, bge, bg
  reg1, reg2, addr
dbz
  reg, addr
* Pseudoinstructions: These instructions can be synthesized with a single different instruction

## Slide 4: Logic Instruction Details
and rA, rB bitwise ANDs contents of rA and rB, storing result in rA
or rA, rB bitwise ORs contents of rA and rB, storing result in rA
xor rA, rB bitwise XORs contents of rA and rB, storing result in rA
inv rA flip all bits of rA, storing result in rA
shl rA, imm bitwise left shift of rA by imm bits, storing result in rA
  for imm < 0 or imm >= 16, rA will be 0x0000
shr rA, imm bitwise right shift of rA by imm bits, storing result in rA
  for imm < 0 or imm >= 16, rA will be 0x0000

## Slide 5: Arithmetic Instruction Details
add rA, rB adds contents of rA and rB, storing result in rA
sub rA, rB subtracts contents of rA and rB, storing result in rA
mult rA, rB multiplies contents of rA and rB, storing result in rA
div rA, rB divides contents of rA and rB, storing quotient in rA
mod rA, rB divides contents of rA and rB, storing remainder in rA
neg rA negates contents of rA, storing remainder in rA
inc rA increments contents of rA, storing remainder in rA
dec rA decrements contents of rA, storing remainder in rA

## Slide 6: Data Instruction Details
set rA, imm sets contents of rA to imm
copy rA, rB sets contents of rA to the same as rB
load rA, addr sets contents rA to the contents of memory[addr]
stor addr, rA sets the contents of memory[addr] to rA
pload rA, rB sets contents rA to the contents of memory[rB]
pstor rA, rB sets the contents of memory[rA] to rB
push rA sets contents of rA to top of stack and decrements SP
pop rA sets contents of rA from the top of the stack and increments SP

## Slide 7: Control Instruction Details
call addr pushes next PC to stack and jumps to code at memory[addr]
ret* pops PC from stack to return from prior call
  same as "pop pc"
jmp addr* sets PC to addr
  same as either "set pc, addr" or "je r0, r0, addr"
* Pseudoinstructions: These instructions can be synthesized with a single different instruction

## Slide 8: Control Instruction Details (continued)
jl rA, rB, addr sets PC to addr if rA < rB
jle rA, rB, addr sets PC to addr if rA <= rB
je rA, rB, addr sets PC to addr if rA == rB
jne rA, rB, addr sets PC to addr if rA != rB
jge rA, rB, addr sets PC to addr if rA >= rB
jg rA, rB, addr sets PC to addr if rA > rB

## Slide 9: Instruction Encodings
15
14
13
12
11
10
9
8
7
6
5
4
3
2
1
0
Opcode
rA
rB
unused/reserved
1st instruction word
15
14
13
12
11
10
9
8
7
6
5
4
3
2
1
0
imm (immediate)
or
addr (address)
2nd instruction word

## Slide 10: Instruction Opcodes
Instr. | Opcode |  | Instr. | Opcode |  | Instr. | Opcode
set | 0 |  | mult | 10 |  | shl | 20
copy | 1 |  | div | 11 |  | shr | 21
load | 2 |  | mod | 12 |  | call | 22
stor | 3 |  | neg | 13 |  | jl | 23
pload | 4 |  | inc | 14 |  | jle | 24
pstor | 5 |  | dec | 15 |  | je | 25
push | 6 |  | and | 16 |  | jne | 26
pop | 7 |  | or | 17 |  | jge | 27
add | 8 |  | xor | 18 |  | jg | 28
sub | 9 |  | inv | 19 |  |  | 
Fun fact: If all words of memory are initialized to 0x0000, then if-ever a program should try to run code beyond that loaded into memory, the fetched instruction will be 0x0000_0000, which decodes into "set pc, 0x0000"... so the program will start over automatically since the first line of code is at 0x0000.